How to change the power supply

LED Spectra Unit classic & special

Step 1 : Loosen the screws which fix the back housing ( Total 8pcs )

Step 2:  Open the back cover ( action softly)         Unplug the connection plug

Step 3: Loosen the screws which fix the power supply to dismantle the power supply

Step 4: Snip off the in lace thread to dismantle the power supply

Unplug the plug

Step 5: Change a new power supply:

Fix the power supply

Make good connection and tie up the wires

Step 6: Connect to the up housing

Step7: Use the screw to assemble the back cover

Remarks:

If half part light up and half part dark :

It may be the power supply that caused such problem.

To confirm the result you can follow up the below steps:

First you can connect all the wires once again to solve the loosening or bad connection problem.

If still doesn’t work then do the next

Second:

You can use the good power supply to replace the damaged one

After replaced, and turn on the grow light to see if that half part lights up.

- If lights up that must be the power supply problem, so we can send you a new one to replace

- If still doesn’t light up that maybe the LED leakage current or other factors, You’re LED Spectra Unit selling point can send them to us. NOTE: With full guaranty if the unit is not older than 1 year(only with original note). If the unit is older than 1 year but not older than 2 year, we pay the repair cost, exclusive the shipping cost to and from the factory. Contact you’re selling point for information.